Comparisons of porousFoam with dissol.

dissol: base grid is 64 pixels wide and 1024 pixels long, with a slot 20 pixels wide and 768 long.
Pe* = 1000 (grid Peclet) and Da* is varied (but < 1).
porousFoam: System width is 1 and length is 16; the slot is 0.3125 (20/60) wide and 12 long.
D = 3.125e-5 corresponding to Pe = 64000 (on scale of W). Note that in porousFoam the initial porosity is 0.5 so this doubles Pe. The reaction rate k = Da (again on scale of W)

Measure the concentration 0.125 0.25, 0.375 0.5 (in units of W) downstream from the tip. Compare upwind and linearUpwind (2nd order) differencing in porousFoam with dissol (upwind).
At large Da* only the linearUpwind scheme is usable. At Da*=0.8 the concentration is measured at 0.02, 0.04, 0.06.

Conclusion: Da* < 0.4 for linearUpwind; Da* < 0.1 for upwind; Da* < 0.05 for dissol.

		linearUpwind			upwind			dissol
Da*	Da	64	128	256	64	128	256	64	128	256
0.05	3.2	0.7410	0.7410	0.7420	0.7321	0.7365	0.7382	0.7561	0.7686	0.7509
		0.5288	0.5280	0.5283	0.5261	0.5267	0.5270	0.5350	0.5429	0.5290
		0.3660	0.3650	0.3649	0.3671	0.3655	0.3651	0.3723	0.3769	0.3662
		0.2491	0.2482	0.2479	0.2521	0.2497	0.2489	0.2556	0.2577	0.2496
0.1	6.4	0.5491	0.5484	0.5491	0.5417	0.5446	0.5461	0.5783	0.5936	0.5655
		0.2780	0.2785	0.2790	0.2835	0.2805	0.2793	0.2931	0.2983	0.2816
		0.1339	0.1330	0.1334	0.1402	0.1362	0.1346	0.1442	0.1449	0.1355
		0.0620	0.0615	0.0618	0.0672	0.0641	0.0629	0.0692	0.0684	0.0632
0.2	12.8	0.3022	0.3005	0.3001	0.3060	0.3028	0.3015	0.3476	0.3590	0.3231
		0.0783	0.0775	0.0773	0.0880	0.0825	0.0800	0.0939	0.0932	0.0813
		0.0179	0.0177	0.0176	0.0228	0.0201	0.0189	0.0241	0.0227	0.0191
		0.0038	0.0038	0.0038	0.0056	0.0046	0.0042	0.0059	0.0052	0.0042
0.4	25.6	0.0917	0.0902	0.0902	0.1087	0.0994	0.0949	0.1378	0.1381	0.1087
		0.0060	0.0060	0.0060	0.0107	0.0081	0.0070	0.0120	0.0103	0.0073
		0.0003	0.0003	0.0003	0.0009	0.0005	0.0004	0.0010	0.0007	0.0004
		0.0000	0.0000	0.0000	0.0001	0.0000	0.0000	0.0000	0.0000	0.0000
0.8	51.2	0.5142	0.4911	0.4784	0.4625	0.4652	0.4677
		0.2569	0.2302	0.2258	0.2581	0.2397	0.2326
		0.1174	0.1076	0.1056	0.1410	0.1239	0.1147